## Slide 1: EX1904
Objectives
  Record raw acoustic time series data
    Provide a baseline for comparison to WHOI micromodem processed data
    Development of beamforming for independent angle and range calculations
    Determine viability of hardware for multichannel, high frequency recording

## Slide 2: EX1904
Test Configuration
  Raspberry Pi Model 3B+
    5V power from distribution board
    Ethernet
    USB to DAQ
    SSH enabled
  MCC USB-1608-FS-Plus DAQ
    Four hydrophone channels and PPS
    100K samples/channel/second max
    400K samples/second aggregate max
  Python based software developed from manufacturer’s library

## Slide 3: EX1904
Observations
  Raspberry Pi 3B+ presented a hardware bottleneck which limited maximum recording rate
  Raspberry Pi 3B+ does not have a real time clock and requires an NTP server
  Array circuitry includes a pre-amp, necessitating bias resistors
Recordings
  First two days of recording were affected by the lack of DC bias control
  Third day successful
    2 hours of recording 5 channels at 45K samples/channel/second
    2 hours of recording Channels 1-3 at 70K samples/channel/second

## Slide 4
25 kHz
iUSBL
10 kHz
iUSBL
Ship’s USBL
ROV response